## Slide 1: Sterility Testing: Traditional & Rapid Methods
A Presentation by: Vamsi Krishna .J

## Slide 2: Sterility Testing
Sterility Testing :
Definition: Sterility testing is a critical microbiology test performed to confirm that a drug product or medical device is free from viable contaminating microorganisms.
Purpose: Patient Safety: Essential for parenteral (injectable) products; contaminants can cause may death.
Regulatory Compliance: Required by global pharmacopeias (USP <71>, EP 2.6.1).
Quality Assurance: Ensures the manufacturing process remains in a "state of control."
Contamination Control Strategy. It provides the final verification that the technical and organizational controls (like cleanroom design and personnel training) are effectively preventing microbial ingress.

## Slide 3: Traditional Methods & Limitations
Current Methods:
1. Membrane Filtration :The preferred method for filterable liquids and soluble products.
Principle: The product is passed through a sterile 0.45-micron membrane filter, which retains any microbial contaminants on the surface.
Procedure:
  The sample is filtered under aseptic conditions.
  The membrane is then aseptically cut into two halves.
  Incubation:
    One half is immersed in Soybean Casein Digest Medium (SCDM) (to detect aerobic bacteria and fungi).
    The other half is immersed in Fluid Thioglycollate Medium (FTGM) (to detect anaerobic and some aerobic bacteria).
Applications: Primarily used for Pre-filled Syringes (PFS), large and small volume parenterals (finished products), and oils/ointments that can be dissolved.

## Slide 4: Traditional Methods & Limitations
2. Direct Inoculation :
The standard method for products that cannot be easily filtered.
Principle: The test sample is introduced directly into the culture media (SCDM and FTGM).
Procedure:
  The volume of the product should not exceed 10% of the volume of the medium to avoid diluting the nutrients or carrying over antimicrobial activity.
  The samples are incubated for a specified period (usually 14 days) to observe for turbidity (growth).
Applications: Mainly used for solid articles and non-filterable materials, including:
  Rubber stoppers and closures.
  Surgical gloves and medical devices.
  Empty vials and glass containers.
  Opaque liquids or suspensions.
The Limitations:
Time-to-Result: Mandatory 14-day incubation period.
Subjectivity: Relies on human eye to detect "turbidity" , leading to potential error.

## Slide 5: Sterility Failure & The Shift to RMM
What happens in a Sterility Failure?
Immediate Root Cause Analysis (RCA) and OOS (Out of Specification) investigation.
The entire batch must be quarantined or destroyed, costing millions.
The Solution: Rapid Microbial Methods (RMM):
Instead of waiting for 14 days of "growth" to be seen by the eye, we use technology to detect growth at the cellular level.
Early detection (Days 3–7) allows for faster investigations and reduces "at-risk" manufacturing.
Proactive Risk Management: Acts as an "Early Warning System" for high-value products like Cell & Gene Therapy.
Faster Intervention: Detects contamination in days (not weeks), allowing manufacturers to fix issues before the entire batch is lost.

## Slide 6: Modern Standards: USP <72> and <73>
Official Status: As of August 2025, these chapters are now Official.
USP <72> (Growth-Based RMM): * Focuses on automated systems like BACT/ALERT® 3D.
Detects CO2 production. Results often achieved in half the time of USP <71>.
USP <73> (Non-Growth-Based RMM):
Focuses on technologies like Solid-Phase Cytometry (SCANRDI®).
Results in hours (Same-day release).
Method Suitability & The "10 CFU" Challenge
Point: Success depends on proving the method can detect very low levels of contamination (NMT 100 CFU, with a target of 10 CFU). We apply the Poisson Distribution to justify statistical variations in low-count inoculums
The Benefit: Unlike manual USP <71> testing, which relies on paper logs, USP <72>/<73> systems ensure that all data is traceable, unalterable, and "Inspection Ready" at all times.

## Slide 7: Conclusion
Standardization: Fully embracing the official status of USP <72> and <73> to ensure global regulatory alignment in 2026.
Patient Centricity: Prioritizing the rapid delivery of life-saving medicines, particularly for patients requiring time-sensitive therapies.
Operational Excellence: Modernizing the microbiology lab to reduce human error, improve data integrity, and maximize manufacturing uptime.
Data Integrity: Moving toward automated, 21 CFR Part 11 compliant systems that provide "Audit-Ready" results at all times.

## Slide 8: THANKYOU
Any Questions ?
Please feel free to share your thoughts or inquiries.
Vamsi Krishna .J